## Slide 1: SIG Me (SIG auto-tunnel for routers)
Nick Russo, Steven McNutt
Customer Delivery Engineering Tech Leader/ Systems Architect
Team SecureY
SecureX Orchestration Hackathon 2021

## Slide 2: Speed is the ultimate weapon in business

## Slide 3: Sig Autotunnel for IOS-XE
  Problem Statement
    There is a large installed base of ISR/ASR1k routers that are running classic designs such as DMVPN. These customers may want the benefits of SASE/NAAS but may not be able to employ SD-WAN due to cost, complexity, or other constraints. Also there may be an urgent need such as Incident Response.
  Solution
    Leverage SXO as an engine to take device inventory as input and drive a provisioner which automatically configures and verifies SIG deployment across the network, quickly.
    SXO provides a basis for IT Operations to quickly create robust, flexible, highly scalable distributed systems architectures for automated solution deployments.

## Slide 4: Classic Branch Design
Internet
On-Prem
Branch Routers
Datacenter Backhaul
  DMVPN network w/Internet backhaul
    Branch Internet traffic backhauled to datacenter.
    Leverages powerful central firewalls for traffic inspection
    Introduces latency
    Problems in the DC affect entire network

## Slide 5: Solution Architecture
Umbrella
Internet
On-Prem
Remote Connector
Provisioner
Device
Inventory
Orchestrator
Branch Routers
Datacenter Backhaul
1
2
3
4
5
2
5
1
3
4
Load routers from DB
Provision request
SIG Create Tunnel
Configure Router
Probe for tunnel up
6
Backup Path if SIG goes down
6

## Slide 6: Solution Architecture Detail
LOAD INVENTORY
Retrieve device list from database
PROVISION REQUEST
Send Umbrella provisioning request to Sidecar
CREATE SIG TUNNEL
Use Umbrella API to create a tunnel.
CONFIGURE ROUTER
Configure router
Poll for status
SXO periodically checks sidecar for status of provisioning requests
Provision complete
SXO has received final status on all provisioning requests. Workflow exits.
If tunnel already exists, generate new pre-shared key
Store task IDs in Table
Probe Sig tunnel for liveness
Output provisioning status
ORCHESTRATION
Device Database
Provisioner
Cisco Umbrella
Notes: I will also share a workflow – which you can either run as your own ‘playbook’ or modify to be as simple or complex as your needs merit.
Let’s see how we can achieve this automation by using the power of APIs, how we could further minimize the human intervention and make this an automated process. SecureX orchestrator enables you to create automated workflows to deliver further value. The workflow below can be modified for any IOC source.
  Inspect API – pull observables out of formatted or unformatted text.
  Enrich API – search for additional information about those observables. Also contains Refer endpoint for pivoting into other products.
  Response API – take actions on observables (for example, add to blocklist).
Case Management – by creating a new casebook the first time any targets are found. On subsequent runs keep updating the casebook if targets found.

## Slide 7: Outcomes/components/Content Links
  Key customer outcomes
    Automate network-wide rollout of Umbrella SIG on a traditional WAN in a matter of minutes.
    Demonstrate the potential of SXO as an IT Operations platform
  Solution Components:
    Device inventory Database, SXO remote connector, SIG provisioner sidecar, Umbrella SIG.
  Example repo:
    Tbd (awaiting access to internal github)
  Example video:

## Slide 8: Best Practices
  Concurrency
    Provisioner handles requests asynchronously
    50 concurrent tasks by default – tunable
    This thing can configure a lot of routers really fast. 
  Descriptive naming:
    Control logic
    Activity names